How Batteries Work

Batteries are all over the place -- in our cars, our PCs, laptops, portable MP3 players and cell phones. A battery is essentially a can full of chemicals that produce electrons. Chemical reactions that produce electrons are called electrochemical reactions. In this article, you'll learn all about batteries -- from the basic concept at work to the actual chemistry going on inside a battery to what the future holds for batteries and possible power sources that could replace them!

If you look at any battery, you'll notice that it has two terminals. One terminal is marked (+), or positive, while the other is marked (-), or negative. In an AA, C or D cell (normal flashlight batteries), the ends of the battery are the terminals. In a large car battery, there are two heavy lead posts that act as the terminals.

Electrons collect on the negative terminal of the battery. If you connect a wire between the negative and positive terminals, the electrons will flow from the negative to the positive terminal as fast as they can (and wear out the battery very quickly -- this also tends to be dangerous, especially with large batteries, so it is not something you want to be doing). Normally, you connect some type of load to the battery using the wire. The load might be something like a light bulb, a motor or an electronic circuit like a radio.

Inside the battery itself, a chemical reaction produces the electrons. The speed of electron production by this chemical reaction (the battery's internal resistance) controls how many electrons can flow between the terminals. Electrons flow from the battery into a wire, and must travel from the negative to the positive terminal for the chemical reaction to take place. That is why a battery can sit on a shelf for a year and still have plenty of power -- unless electrons are flowing from the negative to the positive terminal, the chemical reaction does not take place. Once you connect a wire, the reaction starts.

The first battery was created by Alessandro Volta in 1800. To create his battery, he made a stack by alternating layers of zinc, blotting paper soaked in salt water, and silver, like this:

This arrangement was known as a voltaic pile. The top and bottom layers of the pile must be different metals, as shown. If you attach a wire to the top and bottom of the pile, you can measure a voltage and a current from the pile. The pile can be stacked as high as you like, and each layer will increase the voltage by a fixed amount.

Could blood be used to power batteries?

Batteries are practically essential devices but present a whole host of problems. Over time they can have trouble retaining a charge. Some stop working altogether. Others overheat or leak or even explode. They're also rigid and sometimes bulky. Then how about, instead of your standard AA or lithium-ion, a flexible, incredibly thin battery that could be powered by blood or sweat? Seems like an improvement, right

A group of scientists at Rensselaer Polytechnic Institute claims they've created just such a battery, one that uses the electrolytes naturally found in bodily fluids. The results of the research, detailed in the Aug. 13, 2007, issue of the Proceedings of the National Academy of Sciences, are generating some excitement as part of a new crop of "bio-batteries" that run off of bodily fluids or other organic compounds. (The RPI team claims that theirs could even run on tears or urine.)

The battery is not only as thin as paper; it essentially is paper. At least 90 percent of the battery is made from cellulose, which makes up traditional paper and other paper products [source: RPI]. Aligned carbon nanotubes make up the other 10 percent, give the paper its conductive abilities and also make it black. The nanotubes are imprinted in the very fabric of the paper, creating what's called a nanocomposite paper. One of the paper's authors said that the battery "looks, feels and weighs the same as paper" [source: RPI].

The battery's paper-like construction grants it significant flexibility. The RPI research team believes that the battery could, in the future, be printed in long sheets, which could then be cut into small, custom-shaped batteries. The nanocomposite paper can have holes poked in it or be cut into unusual shapes and continue to function. Several sheets could be lumped together to power medical implants, such as pacemakers, artificial hearts or advanced prosthetics. The battery would easily fit under the skin without causing any discomfort.

Because the ionic liquid used doesn't freeze or evaporate like water, the battery could be employed at a wide range of temperatures: from -100 degrees Fahrenheit up to 300 degrees Fahrenheit. Its temperature resistance and light weight mean that manufacturers of automobiles and airplanes -- both of which require light, durable materials -- may come calling.

The researchers behind the battery claim that their device is unique because it can act "as both a high-energy battery and a high-power supercapacitor" [source: RPI]. Supercapacitors allow for large, quick bursts of energy, potentially extending the technology's already wide range of applications.

The battery, which is considered environmentally friendly because of its lack of chemicals and high cellulose content, was announced in the summer of 2007, but it may be years before it's ready to stream off production lines in long sheets. The RPI research team says that, in the meantime, they're trying to boost the battery's efficiency and to figure out the best method for production.