Asymmetric digital subscriber line

Asymmetric digital subscriber line (ADSL) is a type of digital subscriber line technology, a data communications technology that enables faster data transmission over copper telephone lines than a conventional voiceband modem can provide. It does this by utilizing frequencies that are not used by a voice telephone call. A splitter, or DSL filter, allows a single telephone connection to be used for both ADSL service and voice calls at the same time. ADSL can generally only be distributed over short distances from the telephone exchange, typically less than 4 kilometres (2 mi), but has been known to exceed 8 kilometres (5 mi) if the originally laid wire gauge allows for further distribution.

At the telephone exchange the line generally terminates at a digital subscriber line access multiplexer (DSLAM) where another frequency splitter separates the voice band signal for the conventional phone network. Data carried by the ADSL are typically routed over the telephone company's data network and eventually reach a conventional Internet Protocol network.

Overview

ADSL differs from the less common symmetric digital subscriber line (SDSL) in that bandwidth (and bit rate) is greater toward the customer premises (known as downstream) than the reverse (known as upstream). This is why it is called asymmetric. Providers usually market ADSL as a service for consumers to provide Internet access in a relatively passive mode: able to use the higher speed direction for the download from the Internet but not needing to run servers that would require high speed in the other direction.

There are both technical and marketing reasons why ADSL is in many places the most common type offered to home users. On the technical side, there is likely to be more crosstalk from other circuits at the DSLAM end (where the wires from many local loops are close to each other) than at the customer premises. Thus the upload signal is weakest at the noisiest part of the local loop, while the download signal is strongest at the noisiest part of the local loop. It therefore makes technical sense to have the DSLAM transmit at a higher bit rate than does the modem on the customer end. Since the typical home user in fact does prefer a higher download speed, the telephone companies chose to make a virtue out of necessity, hence ADSL. On the marketing side, limiting upload speeds limits the attractiveness of this service to business customers, often causing them to purchase higher cost leased line services instead. In this fashion, it segments the digital communications market between business and home users.

Operation

Currently, most ADSL communication is full-duplex. Full-duplex ADSL communication is usually achieved on a wire pair by either frequency-division duplex (FDD), echo-cancelling duplex (ECD), or time-division duplex (TDD). FDD uses two separate frequency bands, referred to as the upstream and downstream bands. The upstream band is used for communication from the end user to the telephone central office. The downstream band is used for communicating from the central office to the end user.

With standard ADSL (annex A), the band from 26.000 kHz to 137.825 kHz is used for upstream communication, while 138 kHz – 1104 kHz is used for downstream communication. Under the usual DMT scheme, each of these is further divided into smaller frequency channels of 4.3125 kHz. These frequency channels are sometimes termed bins. During initial training to optimize transmission quality and speed, the ADSL modem tests each of the bins to determine the signal-to-noise ratio at each bin's frequency. Distance from the telephone exchange, cable characteristics, interference from AM radio stations, and local interference and electrical noise at the modem's location can adversely affect the signal-to-noise ratio at particular frequencies. Bins for frequencies exhibiting a reduced signal-to-noise ratio will be used at a lower throughput rate or not at all; this reduces the maximum link capacity but allows the modem to maintain an adequate connection. The DSL modem will make a plan on how to exploit each of the bins, sometimes termed "bits per bin" allocation. Those bins that have a good signal-to-noise ratio (SNR) will be chosen to transmit signals chosen from a greater number of possible encoded values (this range of possibilities equating to more bits of data sent) in each main clock cycle. The number of possibilities must not be so large that the receiver might incorrectly decode which one was intended in the presence of noise. Noisy bins may only be required to carry as few as two bits, a choice from only one of four possible patterns, or only one bit per bin in the case of ADSL2+, and very noisy bins are not used at all. If the pattern of noise versus frequencies heard in the bins changes, the DSL modem can alter the bits-per-bin allocations, in a process called "bitswap", where bins that have become more noisy are only required to carry fewer bits and other channels will be chosen to be given a higher burden. The data transfer capacity the DSL modem therefore reports is determined by the total of the bits-per-bin allocations of all the bins combined. Higher signal-to-noise ratios and more bins being in use gives a higher total link capacity, while lower signal-to-noise ratios or fewer bins being used gives a low link capacity.

The total maximum capacity derived from summing the bits-per-bins is reported by DSL modems and is sometimes termed sync rate. This will always be rather misleading, as the true maximum link capacity for user data transfer rate will be significantly lower; because extra data are transmitted that are termed protocol overhead, reduced figures for PPPoA connections of around 84-87 percent, at most, being common. In addition, some ISPs will have traffic policies that limit maximum transfer rates further in the networks beyond the exchange, and traffic congestion on the Internet, heavy loading on servers and slowness or inefficiency in customers' computers may all contribute to reductions below the maximum attainable. When a wireless access point is used, low or unstable wireless signal quality can also cause reduction or fluctuation of actual speed.