Shapers and Planers

The shaper (поперечно-строгальный станок) is used mainly to produce different flat surfaces. The tool slides against the stationary workpiece and cuts on one stroke, returns to its starting position, and then cuts on the next stroke after a slight lateral displacement. In general, the shaper can make any surface having straight-line elements. It uses only one cutting-tool and is relatively slow, because the return stroke is idle. That is why the shaper is seldom found on a mass production line. It is, however, valuable for tool production and for workshops where flexibility is important and relative slowness is unimportant.

The planet (продольно-строгальный станок) is the largest of the reciprocating machine tools. It differs from the shaper, which moves a tool past a fixed workpiece because the planer moves the workpiece to expose a new section to the tool. Like the shaper, the planet is intended to produce vertical, horizontal, or diagonal cuts. It is also possible to mount several tools at one time in any or all tool holders of a planet to execute multiple simultaneous cuts.

Grinders.

Grinders (шлифовальные станки) remove metal by a rotating abrasive wheel. The wheel is composed of many small grains of abrasive, bonded together, with each grain acting as a miniature cutting tool. The process gives very smooth and accurate finishes. Only a small amount of material is removed at each pass of the wheel, so grinding machines require fine wheel requlation. The pressure of the wheel against the workpiece is usually very light, so that grinding can be carried out on fragile materials that cannot be machined by other conventional devices.

Ответить на вопросы письменно к данному тексту.

- What is the shape of a cutter in a milling machine?

- What moves in a milling machine, a table or a cutter?

- What possible movements has the table of a milling machine?

- What king of surfaces and shapes may be machined by a milling machine?

- What can we use a drilling machine for?

- What kinds of drilling machines exist?

- What is rotated while boring, a cutter or a work-piece?

- Describe the work of a shaper (planer).

- What must be done to execute multiple simultaneous cuts on a planer?

- What is the working tool in a grinder?

- Can we obtain a very smooth surface after grinding and why?

- Can we grind fragile materials and why?